## Slide 1
November 2023
Proposal for whole set of Fidelity Prime Catalytic Converter and Front Muffler
ایران دلکو در اندیشه آسمانی آبی...

## Slide 2
1
Substrate Change
Name | Substrate Specification according to drawing and sample |  |  | Substrate Specification of Iran Delco's suggestion |  | 
 | Diameter (mm) | Length (mm) | Cell Specification (CPSI/Mil) | Diameter (mm) | Length (mm) | Cell Specification (CPSI/Mil)
Fidelity Pre Catalyst | Ø105.7 | 152.4 | 600/3 | - | - | -
Fidelity Main Catalyst | Ø118.4 | 100 | 400/6 | - | - | -
Dignity Prestige Catalyst |  | 152.4 | 750/3 | - | - | -
Dignity Prime Front Substarte |  | 64 | 600/6 | Ø118.4 | 64 | 600/4
Dignity Prime Rear Substarte |  | 100 | 400/6 | - | - | -

## Slide 3
Material Changes
2
Raw | Part name | Material according to customer's drawing | Iran Delco suggestion | Picture | Reason
1 | Bracket | SUS 409L,T=4mm | SUS 430,T=4mm |  | OEM materials in these parts are not available in Iran, and It is not possible to supply in the short time due to limitation for minimum order amount of material.
 |  | EN10088-2 | EN10088-2 |  | 
2 | Bracket | SUS 409L,T=4mm | SUS 430,T=4mm |  | 
 |  | EN10088-2 | EN10088-2 |  | 
3 | Intake flange | SUS 410,T=10mm | SUS 304L,T=10mm |  | 
 |  | EN10088-2 | EN10088-2 |  | 
4 | Head shield | SUS 430,T=0.15mm | Emboss SUS 304,T=0.25-0.3mm |  | 
 |  | EN10088-2 | or SUS 409L,T=0.6mm |  | 
5 | Intake and outlet pipe of down pipe ASSY | SUS 409L, Ø55 T=1.2mm | SUS 409L, Ø54 T=1.5mm |  | 
 |  | EN10088-2 | EN10088-2 |  | 

## Slide 4
Grade | C | Si | Mn | P | S | Cr
SUS 409L(1.4512) | 0.03 | 1 | 1 | 0.04 | 0.015 | 10.5 to 12.5
SUS 430(1.4016) | 0.08 | 1 | 1 | 0.04 | 0.015 | 16 to 18
According to EN10088-2 standard
Comparison chemical characteristics
3
Comparison mechanical and chemical characteristics between stainless steel SUS 409L and SUS 430
Material Changes
Regarding chemical characteristics which you can find in the upper table, the Chromium ingredient of SUS 430 is bigger than SUS409L. In this way, the SUS430 has better corrosion and heat resistance.

## Slide 5
4
Material Changes
Comparison corrosion resistance
Comparison mechanical and chemical characteristics between stainless steel SUS 409L and SUS 430
Chromium percentage to corrosion rate
Regarding the upper charts, if the Chromium ingredient increases, the corrosion resistance will increase.

## Slide 6
Grade | Tensile Strength (Mpa) | Yield Strength (Mpa) | %Elongation
430 | 450 to 600 | 260 | 20
409 | 380 to 560 | 220 | 25
5
Comparison heat resistance
Comparison mechanical and chemical characteristics between stainless steel SUS 409L and SUS 430
Material Changes
Comparison mechanical characteristics
In conclusion, that is obvious the SUS430 has a better chemical and mechanical characteristics in comparison with SUS409L, and also it is more expensive than SUS409L. By the way, at this time, purchasing that specific material with 4mm thickness, it is unreachable for Iran Delco Co.
SUS430: It has better heat resistance compared to SUS409L and can withstand higher temperatures without significant loss of mechanical properties. (815°C in comparison with 705°C)
Conclusion of consideration chemical and mechanical characteristics

## Slide 7
6
Tiara Catalytic Converter
AISI 430,Din 1.4016,T=4mm- EN10088-2
Material Changes
Material benchmark in other catalytic converter
Material benchmark of brackets according to Tiara Catalytic Converter (Baic X5) due to the same condition.

## Slide 8
Grade | C | Si | Mn | P | S | Cr
SUS 410(1.4006) | 0.08 to 0.15 | 1 | 1.5 | 0.04 | 0.015 | 11.5 to 13.5
SUS 304(1.4307) | 0.03 | 1 | 2 | 0.045 | 0.015 | 17.5 to 19.5
According to EN10088-2 standard
7
Material Changes
Comparison mechanical and chemical characteristics between stainless steel SUS 410 and SUS 304L
Comparison chemical characteristics
Regarding to position of intake flange and chemical characteristics which you can find in the upper table, the Chromium ingredient of SUS304L is bigger than SUS410. In this way, the SUS304L has better corrosion and heat resistance.

## Slide 9
Chart: 
| 201 | 202 | 301 | 302 | 304 | 308 | 309 | 310 | 316 | 317 | 321 | 330 | 347 | 410 | 416 | 420 | 440 | 405 | 430 | 442 | 446
intermittent | 815 | 815 | 840 | 870 | 870 | 925 | 980 | 1035 | 870 | 870 | 870 | 1035 | 870 | 815 | 760 | 735 | 815 | 815 | 870 | 1035 | 1175
Continuous | 845 | 845 | 900 | 925 | 952 | 980 | 1095 | 1150 | 925 | 925 | 925 | 1150 | 925 | 705 | 675 | 620 | 760 | 705 | 815 | 980 | 1095
8
Material Changes
Comparison mechanical and chemical characteristics between stainless steel SUS 410 and SUS 304L
Comparison chemical characteristics
According to upper chart, the SUS304L can resist higher temperature in comparison with SUS410

## Slide 10
Grade | Tensile Strength (Mpa) | %Elongation
410 | Max 600 | 20
304L | 520 to 700 | 45
9
Material Changes
Comparison mechanical and chemical characteristics between stainless steel SUS 410 and SUS 304L
Comparison mechanical characteristics
According to EN10088-2 standard
In conclusion, that is obvious the SUS304L has a better chemical and mechanical characteristics in comparison with SUS410, and also it is more expensive than SUS410. By the way, at this time, purchasing that specific material, it is unreachable for Iran Delco Co.
Conclusion of consideration chemical and mechanical characteristics

## Slide 11
10
EF7 TC Manifold
Material Changes
Material benchmark in other catalytic converter
Material benchmark of Intake Flange according to EF7 TC Manifold (IKCO-FEV design) and Shahin Catalytic Converter (Saipa Company) due to the same condition.
Shahin Catalytic Converter

## Slide 12
نوار زمان پروژه
11
Planning
Summary planning of whole set of Fidelity Prime Catalytic Converter
Summary planning of whole set of Fidelity Prime Catalytic Converter |  | 
Part Name | First off tool sample | First Off Process
Pre Catalyst ASSY | 27-Apr-2024 | 02-July-2024
Pipe Down ASSY | 24-Feb-2024 | 22-Jun-2024
Main Catalyst Converter and Front Muffler ASSY | 13-Mar-2024 | 25-Jun-2024

## Slide 13
نوار زمان پروژه
Receive technical documents
July
August
September
October
November
December
January
February
March
August
July
Jun
May
April
Jun
Preparation of price analysis
MOM with customer
Inquiry from Supplier
Prototype sample and replacement in CKD
Catalyst destruction and extraction
Set the order for substrate
Starting the catalyst equipment
The end of manufacturing
mold
First off tool sample
First off process
Sop
12
Φ105.7x152.4 600CPSI,3Mil
Receiving the sample of substrate
Receiving the substrate cargo
2023-2024
Planning
Pre Catalyst ASSY planning by the detail
The end of manufacturing
production fixtures
The end of manufacturing
checking fixtures

## Slide 14
نوار زمان پروژه
The end of manufacturing checking fixtures
The end of manufacturing production fixtures
First off tool sample
13
2023-2024
July
August
September
October
November
December
January
February
March
August
July
Jun
May
April
Jun
Receive technical documents
Preparation of price analysis
MOM with customer
Inquiry from Supplier
Prototype sample and replacement in CKD
Catalyst destruction and extraction
Starting the catalyst equipment
The end of manufacturing mold
The end of manufacturing checking fixtures
The end of manufacturing production fixtures
First off process
Receiving the substrate cargo
2023-2024
Planning
Pipe Down ASSY planning by the detail
First off process
Set the order for Flexible
Receiving the substrate cargo

## Slide 15
نوار زمان پروژه
The end of manufacturing mold
The end of manufacturing checking fixtures
The end of manufacturing production fixtures
First off tool sample
First off process
14
Φ118.4x100
400CPSi,6Mil
Receiving the substrate cargo
2023-2024
July
August
September
October
November
December
January
February
March
August
July
Jun
May
April
Jun
Receive technical documents
Preparation of price analysis
MOM with customer
Inquiry from Supplier
Prototype sample and replacement in CKD
Catalyst destruction and extraction
Set the order for substrate
Starting the catalyst equipment
Planning
Main Catalyst Converter and Front Muffler ASSY planning by the detail
Receiving the sample of substrate